Code Notes for Aerofoil and Cutter
# Introduction
This document contains a set of notes for the code in the Aerofoil and Cutter programs. It is not intended to be a complete description of all the classes, more a set of notes of the core classes and overall principles of operation.
# Aerofoil

## Cutter Axes
X and Y axes are in the vertical plane – i.e. a wing section is plotted in the X/Y plane. The right hand side set of coordinates is quite often referred to as U/V. 0/0 is at the front/bottom of the cutter or bottom left of the screen. Z is the distance from the left hand gantry.
## Basic Aerofoils

Aerofoil data files are stored as a sequence of coordinates that start at the trailing edge with x=1 and continue over the upper surface to the leading edge (x=0) and back along the undersurface back to the trailing edge. Note then that the set of points all have x-coordinates that lie within the range 0..1 i.e. the basic aerofoil section is 1 unit long.

Splines are then fitted to the array of points read in from disk ( CSpline class). The spline converts the point array into a parametric spline – both X and Y are set to become a function of a 3rd parameter U. U varies between 0 and 1 to generate the aerofoil section from trailing edge, over the top surface and back round to the trailing edge on the bottom. CSpline also allows the tangent (and hence normal vector) to be calculated at any point. This is useful when allowing for skin thickness.

Given the aerofoil is only 1 unit long it needs to be scaled for a given chord. CTransform class does this and also optionally applies a thickness modifier, a rotation (for washout) and a translation for height and sweep. When calculating a wing section most dimensions are scaled down by the chord to map them into the “aerofoil space” of 1 unit long.

When cutting a wing section the program searches for the value of U at the leading edge. This may be slightly different for root and tip if different sections are used. These values are then used to create a “Frame” object to control the overall cutting. Other things such as LE/TE, spars, cutouts etc have “Intercepts” created for them. An Intercept basically says at a given value of U do some other cutting process. Between Intercepts it’s just a case of cutting the basic wing section.

# Structure, Cutters and Plotters
Structure classes all describe a “thing” that can be cut or plotted such as a wing, an ellipse pair, DXF CAD information or a point structure. They all derive from CStructure. CStructure has the concept of “span” - for a wing it’s the distance between the ends of the core, for an ellipse pair it’s the distance between the ellipses. Structure classes end to be fairly dumb – they can describe their geometry, load and save themselves but can’t cut or plot.
For plotting to paper, each concrete structure class has a corresponding plotting class derived from CPlotStructure class. The “Plot” classes know how to generate a 2D plot to a COutputDevice
For driving a CNC cutter, each concrete structure class has a corresponding cut class derived from CutStructure class. The “Cut” classes know how to generate a 3D cut to a COutputDevice.
COutputDevice has a number of methods, the main ones being MoveTo and LineTo. These both take a stream index to determine whether the call is for the root or tip and a PointT with the coordinates to move or cut to. Other methods provided greater control over the cutter/plotter.
There are a range of output devices:
For plotting, CLaserJetOutputDevice, CPostscriptOutputDevice are specialist output devices that generate raw HPGL or PostScript respectively. DXFOutputDevice will generate a 2D plot in a DXF CAD file.
BlockCorrectionOutputDevice is a “shim” output device that provides corrections for rotated objects and delegates the output to another output device.
Bounds is a dummy output device that records the x,y,z bounds of the plot/cut.
CutterSimulationOutputDevice simulates a cutter and provides an animated display of how the cutter axes move.
CCNCConnectionOutputDevice and GCodeOutputFile both derive from GCodeOutputDevice - the only difference is how the GCode is written – whether to a network connection or output file respectively.
Finally, WindowsOutputDevice knows how to draw into a Windows device context.
## Cutter Geometry
For any case where x != y or u !=v the wire will be at an angle. To cut a given shape on the sides of the block, the cutter has to move to different positions to ensure that the wire is in the correct position. This is managed by CutterGeometry class – it knows the left hand position, right and position of the block and the width of the cutter. It can then transform a set of x,y,u,v coordinates out from the edges of the block to the cutter itself.
The method to do this is:
blockToAxes(Position<double>& pos, double zl, double zr)

As can be seen, as well as the position, it also takes left and right z values. If either of these are non-zero it uses these as z positions relative to the left of the block for calculating the correct position to move the cutter to. This allows rotated components where the calculated positions aren’t on the sides of the block but lie within it.
CutterGeometry is also used when producing a cut to move each xyz component to the edge of an imaginary block based on the bounding box of the cut. This allows rotated components to be treated as if they lie within a rectangular block aligned with the cutter axes.

## Cutter Simulation
CutterPreviewWindow manages the output display, scroll bars, bitmap etc. The CutterSimulation calls back into the window via plot(…) to do the actual plotting.
CutterSimulationOutputDevice collects the data values for moves/lines and then calls stepTo in the CutterSimulation pCutter when it has a pair.
CutterSimulation simulates a set of discrete steppers and drives these so they step in x/y directions as needed. The main entry point is
stepTo(double x, double y, double u, double v, double zl, double zr)
 which transforms the values using the cutter geometry converts the values into steps and calls moveSteppers to run the virtual steppers. This then calls back into the point plotter to actually draw the points on the bitmap & screen.