# Aerofoil

## Cutter Axes
X and Y axes are in the vertical plane – i.e. a wing section is plotted in the X/Y plane. The right hand side set of coordinates is quite often referred to as U/V. 0/0 is at the front/bottom of the cutter or bottom left of the screen. Z is the distance from the left hand gantry.
## Basic Aerofoils

Aerofoil data files are stored as a sequence of coordinates that start at the trailing edge with x=1 and continue over the upper surface to the leading edge (x=0) and back along the undersurface back to the trailing edge.

Splines

## Cutter Geometry
For any case where x != y or u !=v the wire will be at an angle. To cut a given shape on the sides of the block, the cutter has to move to different positions to ensure that the wire is in the correct position. This is managed by CutterGeometry class – it knows the left hand position, right and position of the block and the width of the cutter. It can then transform a set of x,y,u,v coordinates out from the edges of the block to the cutter itself.
The method to do this is:
blockToAxes(Position<double>& pos, double zl, double zr)

As can be seen, as well as the position, it also takes left and right z values. If either of these are non-zero it uses these as z positions relative to the left of the block for calculating the correct position to move the cutter to. This allows rotated components where the calculated positions aren’t on the sides of the block but lie within it.
CutterGeometry is also used when producing a cut to move each xyz component to the edge of an imaginary block based on the bounding box of the cut. This allows rotated components to be treated as if they lie within a rectangular block aligned with the cutter axes.

## Cutter Simulation
CutterPreviewWindow manages the output display, scroll bars, bitmap etc. The CutterSimulation calls back into the window via plot(…) to do the actual plotting.
CutterSimulationOutputDevice collects the data values for moves/lines and then calls stepTo in the CutterSimulation pCutter when it has a pair.
CutterSimulation simulates a set of discrete steppers and drives these so they step in x/y directions as needed. The main entry point is
stepTo(double x, double y, double u, double v, double zl, double zr)
 which transforms the values using the cutter geometry converts the values into steps and calls moveSteppers to run the virtual steppers. This then calls back into the point plotter to actually draw the points on the bitmap & screen.